## Slide 1: Implicit numerical solutions

## Slide 2
dT/dt = a d2T/dx2
Approximate time derivative (superscript p index)
dT/dt = [Tmp+1 – Tmp]/Dt
Approximate position derivative (subscript m index)
d2T/dx2 = [Tm+1p – 2Tmp+ Tm-1p]/Dx2 (forward difference)
Tmp+1 = (Dt/aDx2)[Tm+1p + Tm-1p] + [1-(2Dt/aDx2)]Tmp
(2Dt/aDx2)> 1

## Slide 3
Alternative formulation of problem
dT/dt = a d2T/dx2
Same approximate time derivative
dT/dt = [Tmp+1 – Tmp]/Dt
Position derivative is combination of forward and backwards differences
d2T/dx2 = f*[Tm+1p – 2Tmp+ Tm-1p]/Dx2 +
(1-f)*[Tm+1p+1 – 2Tmp+1 + Tm-1p+1]/Dx2
f is an arbitrary weighting factor (0<f<1)

## Slide 4
Inserting these into dT/dt = a d2T/dx2
[Tmp+1 – Tmp]/Dt =
a{f*[Tm+1p – 2Tmp+ Tm-1p]/Dx2 +
(1-f)*[Tm+1p+1 – 2Tmp+1 + Tm-1p+1]/Dx2}
The Crank-Nicholson method uses f=0.5
[Tmp+1 – Tmp]/Dt =
a{0.5*[Tm+1p – 2Tmp+ Tm-1p]/Dx2 +
(0.5)*[Tm+1p+1 – 2Tmp+1 + Tm-1p+1]/Dx2}

## Slide 5
[Tmp+1 – Tmp]/Dt =
a{0.5*[Tm+1p – 2Tmp+ Tm-1p]/Dx2 +
(0.5)*[Tm+1p+1 – 2Tmp+1 + Tm-1p+1]/Dx2}
Re-arranging to put all p+1 terms on left side and defining b = aDt/Dx2
-bTm-1p+1+ 2(1+b) Tmp+1-bTm+1p+1 = bTm-1p + 2(1-b)Tmp+bTm+1p
These are essentially a set of implicit simultaneous equations that can be solved using traditional matrix algebra.

## Slide 6
Using same problem that we did using forward difference,
Dx=0.1, Dt=0.1, a=0.02 b=0.2
x=0 T=440 for all t (boundary condition)
x=0.5 T=350 for all t (boundary condition)
Initially (t=0) for all x, T=350 (initial condition)
p 0 1 2 3 4
m x t 0 0.1 0.2 0.3 0.4
0 0 440 440 440 440 440
1 0.1 350
2 0.2 350
3 0.3 350
4 0.4 350
5 0.5 350 350 350 350 350

## Slide 7: -bTm-1p+1+2(1+b) Tmp+1-bTm+1p+1 = bTm-1p + 2(1-b)Tmp+bTm+1p
p 0 1 2 3 4
m x t 0 0.1 0.2 0.3 0.4
0 0 440 440 440 440 440
1 0.1 350
2 0.2 350
3 0.3 350
4 0.4 350
0.5 350 350 350 350 350
p=0 b=0.2
m=1 -0.2T01+(1+0.2) T11-0.2T21 = 0.2T00 + 2(1-0.2)T10+0.2T20
m=2 -0.2T11+(1+0.2) T21-0.2T31 = 0.2T10 + 2(1-0.2)T20+0.2T30
m=3 -0.2T21+(1+0.2) T31-0.2T41 = 0.2T20 + 2(1-0.2)T30+0.2T40
m=4 -0.2T31+(1+0.2) T41-0.2T51 = 0.2T30 + 2(1-0.2)T40+0.2T50
m=5 -0.2T41+(1+0.2) T51-0.2T61 = 0.2T40 + 2(1-0.2)T50+0.2T60

## Slide 8
p 0 1 2 3 4
m x t 0 0.1 0.2 0.3 0.4
0 0 440 440 440 440 440
1 0.1 350
2 0.2 350
3 0.3 350
4 0.4 350
5 0.5 350 350 350 350 350
p=0
m=1 -0.2T01+(2.4) T11-0.2T21 = 0.2T00 + (1.6)T10+0.2T20
m=2 -0.2T11+(2.4) T21-0.2T31 = 0.2T10 + (1.6)T20+0.2T30
m=3 -0.2T21+(2.4) T31-0.2T41 = 0.2T20 + (1.6)T30+0.2T40
m=4 -0.2T31+(2.4) T41-0.2T51 = 0.2T30 + (1.6)T40+0.2T50
m=5 -0.2T41+(1+0.2) T51-0.2T61 = 0.2T40 + 2(1-0.2)T50+0.2T60 Plug in values for Tm0
-0.2(440)+(2.4) T11-0.2T21 = 0.2(440) + (1.6)(350)+0.2(350)
-0.2T11+(2.4) T21-0.2T31 = 0.2(350) + (1.6)(350)+0.2(350)
-0.2T21+(2.4) T31-0.2T41 = 0.2(350) + (1.6)(350)+0.2(350)
-0.2T31+(2.4) T41-0.2T51 = 0.2(350) + (1.6)(350)+0.2(350)
-0.2T41+(1+0.2) T51 = 0.2(350) + 2(1-0.2)(350)+0.2(350)
2.4 T11-0.2T21 = 0.2*440+0.2(440) + (1.6)(350)+0.2(350)=806
-0.2T11+(2.4) T21-0.2T31 = 0.2(350) + (1.6)(350)+0.2(350)=700
-0.2T21+(2.4) T31-0.2T41 = 0.2(350) + (1.6)(350)+0.2(350)=700
-0.2T31+(2.4) T41-0.2T51 = 0.2(350) + (1.6)(350)+0.2(350)=700
-0.2T41+(1+0.2) T51 = 0.2(350) + 2(1-0.2)(350)+0.2(350)=700

## Slide 9
2.4 T11-0.2T21 + 0 T31 + 0 T41 + 0 T51 = 806
-0.2T11+(2.4) T21-0.2T31 + 0 T41 + 0 T51 =700
0 T11-0.2T21+(2.4) T31-0.2T41 + 0 T51 =700
0 T11 +0 T21 -0.2T31+(2.4) T41-0.2T51 =700
0 T11 +0 T21 + 0 T31 -0.2T41+(2.4) T51 = 700
2.4 -0.2 0 0 0 T11 806
-0.2 2.4 -0.2 0 0 T21 700
0 -0.2 2.4 -0.2 0 * T31 = 700
0 0 -0.2 2.4 -0.2 T41 700
0 0 0 -0.4 2.4 T51 700
A * T = R
T = A-1 *R

## Slide 10
p 0 1 2 3 4
m x t 0 0.1 0.2 0.3 0.4
0 0 440 440 440 440 440
1 0.1 350 365.1
2 0.2 350 350.3
3 0.3 350 350
4 0.4 350 350
0.5 350 350 350 350 350

## Slide 11: -bTm-1p+1+2(1+b) Tmp+1-bTm+1p+1 = bTm-1p + 2(1-b)Tmp+bTm+1p
p 0 1 2 3 4
m x t 0 0.1 0.2 0.3 0.4
0 0 440 440 440 440 440
1 0.1 350 365.1
2 0.2 350 350.3
3 0.3 350 350
0.4 350 350
0.5 350 350 350 350 350
p=1
m=1 -0.2T02+(2.4) T12-0.2T22 = 0.2T01 + (1.6)T11+0.2T21
m=2 -0.2T12+(2.4) T22-0.2T32 = 0.2T11 + (1.6)T21+0.2T31
m=3 -0.2T22+(2.4) T32-0.2T42 = 0.2T21 + (1.6)T31+0.2T41
m=4 -0.2T32+(2.4) T42-0.2T52 = 0.2T31 + (1.6)T41+0.2T51
m=5 -0.2T42+(2.4) T52-0.2T62 = 0.2T41 + 1.6T51+0.2T61

## Slide 12
p 0 1 2 3 4
m x t 0.1 0.2 0.3 0.4
0 0 440 440 440 440 440
1 0.1 350 365.1
2 0.2 350 350.3
  0.3 350 3504
  0.4 350 3505
  0.5 350 350 350 350 350
p=1
m=1 -0.2T02+(2.4) T12-0.2T22 = 0.2T01 + (1.6)T11+0.2T21
m=2 -0.2T12+(2.4) T22-0.2T32 = 0.2T11 + (1.6)T21+0.2T31
m=3 -0.2T22+(2.4) T32-0.2T42 = 0.2T21 + (1.6)T31+0.2T41
m=4 -0.2T32+(2.4) T42-0.2T52 = 0.2T31 + (1.6)T41+0.2T51
m=5 -0.2T42+(2.4) T52-0.2T62 = 0.2T41 + 1.6T51+0.2T61 Plug in values for Tm1
-0.2(440)+(2.4) T12-0.2T22 = 0.2(440) + (1.6)(365.1)+0.2(350.3)
-0.2T12+(2.4) T22-0.2T32 = 0.2(365.1) + (1.6)(350.3)+0.2(350)
-0.2T22+(2.4) T32-0.2T42 = 0.2(350) + (1.6)(300)+0.2(350)
-0.2T32+(2.4) T42-0.2T52 = 0.2(350) + (1.6)(350)+0.2(350)
-0.2T42+(2.4) T52 = 0.2(350) + 1.6(350)+0.2(350)
2.4 T12-0.2T22 = 830.4
-0.2T12+(2.4) T22 -0.2T32 = 705.1
-0.2T22+(2.4) T32-0.2T42 = 700.4
-0.2T32+(2.4) T42-0.2T52 = 700
-0.2T42+(2.4) T52 = 700

## Slide 13
2.4 T12-0.2T22 = 830.4
-0.2T12+(2.4) T22 -0.2T32 = 705.1
-0.2T22+(2.4) T32-0.2T42 = 700.4
-0.2T32+(2.4) T42-0.2T52 = 700
-0.2T42+(2.4) T52-0.2T62 = 700
2.4 -0.2 0 0 0 T12 830.4
-0.2 2.4 -0.2 0 0 T22 705.1
0 -0.2 2.4 -0.2 0 * T32 = 700.4
0 0 -0.2 2.4 -0.2 T42 700
0 0 0 -0.4 2.4 T52 700
A * T = R
T = A-1 *R

## Slide 14
p 0 1 2 3 4
m x t 0 0.1 0.2 0.3 0.4
0 0 440 440 440 440 440
1 0.1 350 365.1 375.5
2 0.2 350 350.3 354.3
3 0.3 350 350 350.54
4 0.4 350 350 350.1
0.5 350 350 350 350 350

## Slide 16: Other C-N presentations
https://en.wikipedia.org/wiki/Crank%E2%80%93Nicolson_method
https://www.youtube.com/watch?v=TSGAxWoNM9o