## Slide 1
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6
Basis: 1 mol of hydrogen entering in stream 1, 100% excess oxygen used
Calculate energy streams 5 and 6

## Slide 2
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6
Define a system
System 1 Fuel cell (calc F5)
System 2 Exhaust heat exchanger (Calc F6)
Component mass balances on system 1
4 components, H,O,W, N
SFjxHj + rxn = F1*xH1+F2*xH2- F3*xH3-F5*xH5 + rxn) = d(Msys*xHsys)/dt
SFjxOj+rxn= F1*xO1+F2*xO2- F3*xO3-F5*xO5 + rxn) = d(Msys*xOsys)/dt
SFjxWj + rxn= F1*xW1+F2*xW2- F3*xW3-F5*xW5 + rxn) = d(Msys*xWsys)/dt
SFjxNj +rxn = F1*xN1+F2*xN2- F3*xN3-F5*xN5 + rxn) = d(Msys*xNsys)/dt
Xij – mass fraction of component I in stream j
Fj – total mass flowrate j
Msys – total mass in system

## Slide 3
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6
Energy balance on system 1
SFjhj+SEj = F1(h1)+F2(h2)-F3(h3)-F5 = d(Msyshsys)/dt
hj = Sxijhj = xHjhHj+xOjhOj+xWjhWj+xNjhNj
SFjxijhij = F1(xH1hH1+xO1hO1+xW1hW1+xN1hN1) + F2(xH2hH2+xO2hO2+xW2hW2+xN2hN2) - F3 (xH3hH3+xO3hO3+xW3hW3+xN3hN3)-F5 = d(Msyshsys)/dt
xij – mass fraction of component I in stream j
Fj – total mass flowrate j
Msys – total mass in system
hj – enthalpy of stream j
hij – specific enthalpy of component i in stream j

## Slide 4
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6
Component mass balances on system 1
SFjxHj + rxn = F1*xH1+F2*xH2- F3*xH3-F5*xH5 + rxn = d(Msys*xHsys)/dt
SFjxOj + rxn = F1*xO1+F2*xO2- F3*xO3-F5*xO5 + rxn = d(Msys*xOsys)/dt
SFjxWj + rxn = F1*xW1+F2*xW2- F3*xW3-F5*xW5 + rxn = d(Msys*xWsys)/dt
SFjxNj + rxn = F1*xN1+F2*xN2- F3*xN3-F5*xN5 + rxn = d(Msys*xNsys)/dt
Basis is F1=2 gm, system at steady state, x = 1, xO2=0.233 xN2=0.767
F2*xO2/MWTO = F1xH1/MWTH (100% excess O, F2 = 32/0.233 = 137.34)
= (Nio-Ni)/ni so mass reacted is xni MWTi = mio-mi = rxn

## Slide 5
Component mass balances on system 1 (colored terms = 0)
F1*xH1+F2*xH2- F3*xH3-F5*xH5 + xnH MWTH = d(Msys*xHsys)/dt
F1*xO1+F2*xO2- F3*xO3-F5*xO5 + xnO MWTO = d(Msys*xOsys)/dt
F1*xW1+F2*xW2- F3*xW3-F5*xW5 + xnO MWTO = d(Msys*xWsys)/dt
F1*xN1+F2*xN2- F3*xN3-F5*xN5 + rxn = d(Msys*xNsys)/dt
F1*xH1+ xnH MWTH = 0
F2*xO2- F3*xO3+ xnO MWTO = 0
F3*xW3 + xnO MWTO = 0
F2*xN2- F3*xN3 = 0
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6

## Slide 6
Component mass balances on system 1
F1*xH1+ xnH MWTH = 0
F2*xO2-F3*xO3+ xnO MWTO = 0
F3*xW3 + xnO MWTO = 0
F2*xN2- F3*xN3 = 0
Knowns:
F1=2, F2=137.34, xH1 = 1, XO2=0.233, XN2=0.767, x=1, all ni, MWTi
(2)(1) + (1)(-1)(2) =0
137.34*(0.233) -F3*xO3+ (1)(-1/2)(32) =0
F3*(xW3) + (1)(1)(18) =0
137.34(.767)- F3*xN3 =0
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6

## Slide 7
137.34*(0.233) -F3*xO3+ (1)(-1/2)(32) =0
F3*(xW3) + (1)(1)(18) =0
137.34(.767)- F3*xN3 =0
F3*xO3 =16 Sxi=1
F3*xW3 = 18
F3*xN3 =105.34
4 unknowns (F3, xO3, xN3, xW3) and 4 equations: can solve
F3=139.34 xO3=0.1148 xN3=0.7560 xW3=0.1292
Know all flowrates and compositions of all streams
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6

## Slide 8
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6
System fuel cell
Energy balance
SFj(Sxij*hij)+SFe = F1(xH1hH1+xO1hO1+xW1hW1+xN1hN1) +
F2(xH2hH2+xO2hO2+xW2hW2+xN2hN2)- F3 (xH3hH3+xO3hO3+xW3hW3+xN3hN3) –F5 = d(Msyshsys)/dt
h = hformation+hthermal+hphase hformation - from tables
hthermal - mCpT
hphase - from tables
Xij – mass fraction of component I in stream j
Fj – total mass flowrate j
Msys – total mass in system
hij – enthalpy of component I in stream j
Fe – energy only streams

## Slide 9
F1(xH1hH1+xO1hO1+xW1hW1+xN1hN1) +F2 (xH2hH2+xO2hO2+xW2hW2+xN2hN2)- F3 (xH3hH3+xO3hO3+xW3hW3+xN3hN3) –F5 = d(Msyshsys)/dt =SFj(Sxij*hij)+SFe
F1(xH1hH1) +F2 (xO2hO2+xN2hN2)- F3 (xO3hO3+xW3hW3+xN3hN3) –F5 = d(Msyshsys)/dt
F1=2 xH1 = 1
F2=137.34 xO2=0.233 xN2=0.767
F3=139.34 xO3=0.1148 xW3=0.1292 xN3=0.7560
Steady state system
2(1)(hH1) +137.34[(0.233)(hO2)+(0.767)(hN2)] - 139.34[(0.1148)(hO3)+(0.1292)(hW3)+(0.756)(hN3)] –F5 = 0
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6

## Slide 10
2(hH1) +137.34[(0.233)(hO2)+(0.767)(hN2)] - 139.34[(0.1148)(hO3)+(0.1292)(hW3)+(0.756)(hN3)] –F5 = 0
h = hformation+hthermal+hphase hformation - from tables
hthermal - mCpT
hphase - from tables
hij = = hijformation+hijthermal+hijphase
Note: for this problem there is no phase change, hence Dhijphase = zero
hij = = hijformation+hijthermal
2(hH1formation+hH1thermal ) +137.34[(0.233)(hO2formation+hO2thermal) +(0.767)(hN2formation+hN2thermal )] - 139.34[(0.1148)(hO3formation+hO3thermal) +(0.1292)(hW3formation+hW3thermal)+(0.756)(hN3formation+hN3thermal )] –F5 = 0
Component | DHf, 298 (kJ/gm) | DGf, 298 (kJ/mol) | Cp (kJ/gm-K) | Tc (K) | Pc (MPa) | w | Molecular weight
Oxygen | 0 | 0 | 0.00088 | 154.6 | 5.043 | 0.022 | 32
Hydrogen | 0 | 0 | 0.015 | 33.3 | 1.297 | -0.215 | 2
Nitrogen | 0 | 0 | 0.0011 | 126.1 | 3.394 | 0.040 | 28
Water | -7.557 | -228.614 | 0.00129 | 647.3 | 22.120 | 0.344 | 18

## Slide 11
2(hH1formation+hH1thermal ) +137.34[(0.233)(hO2formation+hO2thermal) +(0.767)(hN2formation+hN2thermal )] - 139.34[(0.1148)(hO3formation+hO3thermal) +(0.1292)(hW3formation+hW3thermal)+(0.756)(hN3formation+hN3thermal )] –F5 = 0
Hthermal = CpT
2[0+(0.01456)(298)] +
137.34[(0.233)(0+(0.00088)(298)] +(0.767)(0+(0.0011)(298))] - 139.34[(0.1148)(0+(0.00088)(500))] +(0.1292)((-13.435+(0.00179)(500)) +(0.756)(0+(0.0011)(500))] –F5 = 0
51.597+160.766 –F5 = 0
so F5 = 212.363 kJ/2 gm H or 106.18 kJ/gm H
Component | DHf, 298 (kJ/mol) | DGf, 298 (kJ/mol) | Cp (kJ/mol-K) | Tc (K) | Pc (MPa) | w | Molecular weight
Oxygen | 0 | 0 | 0.0281 | 154.6 | 5.043 | 0.022 | 32
Hydrogen | 0 | 0 | 0.0291 | 33.3 | 1.297 | -0.215 | 2
Nitrogen | 0 | 0 | 0.0308 | 126.1 | 3.394 | 0.040 | 28
Water | -241.835 | -228.614 | 0.0323 | 647.3 | 22.120 | 0.344 | 18

## Slide 12
Energy balance on exhaust heat exchanger
139.34[(0.1148)(hO3thermal)+(0.1292)(hW3thermal)+(0.756)(hN3thermal )] -139.34[(0.1148)(hO4thermal)+(0.1292)(hW4thermal)+(0.756)(hN4thermal )] –F6 = 0
Hthermal = CpT
139.34[(0.1148)(0.00088)(500)] +(0.1292)(0.00129)(500) +(0.756)(0.0011)(500)] - 139.34[(0.1148)(0.00088)(298)] +(0.1292)(0.00129)(298) +(0.756)(0.0011)(298)] –F6 = 0
139.34[(0.1148)(0.00088)(500-298)] +(0.1292)(0.00129)(500-298) +(0.756)((0.0011)(500))] –F6 = 0
2.844 +23.404 + 6.508 –F6 = 0 so F6 = 32.757 kJ/gm H
Component | DHf, 298 (kJ/gm) | DGf, 298 (kJ/mol) | Cp (kJ/gm-K) | Tc (K) | Pc (MPa) | w | Molecular weight
Oxygen | 0 | 0 | 0.00088 | 154.6 | 5.043 | 0.022 | 32
Hydrogen | 0 | 0 | 0.015 | 33.3 | 1.297 | -0.215 | 2
Nitrogen | 0 | 0 | 0.0011 | 126.1 | 3.394 | 0.040 | 28
Water | -7.557 | -228.614 | 0.00129 | 647.3 | 22.120 | 0.344 | 18

## Slide 13
If SUV must produce 250 hp then the rate of energy production from the fuel cell must be
250 hp = 186.425 kJ/s
186.425 kJ/s / 106.18 kJ/gm H =
1.756 gm H/s @ 250 hp
65 mile/hr /1.756 gm/s = 10.28 mile/kg
For a 500 mile range, 500 miles / 10.28 mile/kg = 48.62 kg
Density = 48.62 kg/1.5 cubic meters = 32.41 kg/cubic meter
Using Peng-Robinson EOS, at room temperature, this means the pressure in the tank must be almost 700 atm

## Slide 15
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6
Define a system
system 1 Fuel cell
System 2 Exhaust heat exchanger
Component mass balances on system 1
4 components, H,O,W, N
MWTH(F1*xH1+F2*xH2- F3*xH3-F5*xH5 + rxn) = d(MWTHNsys*xHsys)/dt = MWTHSFjxHj
MWTO(F1*xO1+F2*xO2- F3*xO3-F5*xO5 + rxn) = d(MWTOMsys*xOsys)/dt = MWTOSFjxOj
MWTW(F1*xW1+F2*xW2- F3*xW3-F5*xW5 + rxn) = d(MWTWMsys*xWsys)/dt = MWTWSFjxWj
MWTN(F1*xN1+F2*xN2- F3*xN3-F5*xN5 + rxn) = dMWTN (Msys*xNsys)/dt = MWTNSFjxNj
Xij – mole fraction of component I in stream j
Fj – total mole flowrate j
Msys – total mass in system
MWTi – molecular weight of component I
N – total moles

## Slide 16
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6
System fuel cell + exhaust heat exchanger
Energy balance
F1(xH1hH1+xO1hO1+xW1hW1+xN1hN1) +F2 (xH2hH2+xO2hO2+xW2hW2+xN2hN2)- F4 (xH4hH4+xO4hO4+xW4hW4+xN4hN4) –F5 – F6 = d(Msyshsys)/dt =SFj(Sxij*hij)+SFe
h = hformation+hthermal+hphase hformation - from tables
hthermal - mCpT
hphase - from tables
Xij – mass fraction of component I in stream j
Fj – total mass flowrate j
Msys – total mass in system
hij – enthalpy of component I in stream j
Fe – energy only streams

## Slide 17
F1(xH1hH1+xO1hO1+xW1hW1+xN1hN1) +F2 (xH2hH2+xO2hO2+xW2hW2+xN2hN2)- F4 (xH4hH4+xO4hO4+xW4hW4+xN4hN4) –F5 – F6 = d(Msyshsys)/dt =SFj(Sxij*hij)+SFe
F1(xH1hH1) +F2 (xO2hO2+xN2hN2)- F4 (xO4hO4+xW4hW4+xN4hN4) –F5 – F6 = d(Msyshsys)/dt
F1=2 xH1 = 1
F2=137.34 xO2=0.233 xN2=0.767
F4=F3=139.34 xO4=0.1148 xW4=0.1292 xN4=0.7560
Steady state system
2(1)(hH1) +137.34[(0.233)(hO2)+(0.767)(hN2)] - 139.34[(0.1148)(hO4)+(0.1292)(hW4)+(0.756)(hN4)] –F5 – F6 = 0
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6

## Slide 18
2(hH1) +137.34[(0.233)(hO2)+(0.767)(hN2)] - 139.34[(0.1148)(hO4)+(0.1292)(hW4)+(0.756)(hN4)] –F5 – F6 = 0
h = hformation+hthermal+hphase hformation - from tables
hthermal - mCpT
hphase - from tables
hij = = hijformation+hijthermal+hijphase
Note: for this problem there is no phase change, hence Dhijphase = zero
hij = = hijformation+hijthermal
2(hH1formation+hH1thermal ) +137.34[(0.233)(hO2formation+hO2thermal )+(0.767)(hN2formation+hN2thermal )] - 139.34[(0.1148)(hO4formation+hO4thermal) +(0.1292)(hW4formation+hW4thermal)+(0.756)(hijformation+hN4thermal )] –F5 – F6 = 0
Component | DHf, 298 (kJ/mol) | DGf, 298 (kJ/mol) | Cp (kJ/mol-K) | Tc (K) | Pc (MPa) | w | Molecular weight
Oxygen | 0 | 0 | 0.0281 | 154.6 | 5.043 | 0.022 | 32
Hydrogen | 0 | 0 | 0.0291 | 33.3 | 1.297 | -0.215 | 2
Nitrogen | 0 | 0 | 0.0308 | 126.1 | 3.394 | 0.040 | 28
Water | -241.835 | -228.614 | 0.0323 | 647.3 | 22.120 | 0.344 | 18

## Slide 19
H2 + ½ O2 -> H2O
Fuel tank
Hydrogen
0.5 cubic meters
25 deg C
Fuel cell
500 K
1 atm
Exhaust heat exchanger
Energy available to power the SUV
Waste heat to environment
Air (21 mol% O2, 79 mol% N2)
25 deg. C
100% stoichiometric excess
Exhaust gases
25 deg C, 1 atm
1
2
3
4
5
6
Define a system
system 1 Fuel cell
System 2 Exhaust heat exchanger
Component mass balances on system 1
4 components, H,O,W, N
MWTH(F1*xH1+F2*xH2- F3*xH3-F5*xH5 + rxn) = d(MWTHNsys*xHsys)/dt = MWTHSFjxHj
MWTO(F1*xO1+F2*xO2- F3*xO3-F5*xO5 + rxn) = d(MWTOMsys*xOsys)/dt = MWTOSFjxOj
MWTW(F1*xW1+F2*xW2- F3*xW3-F5*xW5 + rxn) = d(MWTWMsys*xWsys)/dt = MWTWSFjxWj
MWTN(F1*xN1+F2*xN2- F3*xN3-F5*xN5 + rxn) = dMWTN (Msys*xNsys)/dt = MWTNSFjxNj
Xij – mole fraction of component I in stream j
Fj – total mole flowrate j
Msys – total mass in system
MWTi – molecular weight of component I
N – total moles

## Slide 20
2(hH1formation+hH1thermal ) +137.34[(0.233)(hO2formation+hO2thermal) +(0.767)(hN2formation+hN2thermal )] - 139.34[(0.1148)(hO4formation+hO4thermal) +(0.1292)(hW4formation+hW4thermal)+(0.756)(hN4formation+hN4thermal )] –F5 – F6 = 0
Hthermal = CpT
2[0+(0.0291)(298)] +137.34[(0.233)(0+(0.0281)(298)] +(0.767)(0+(0.0308)(298))] - 139.34[(0.1148)(0+(0.0281)(298))] +(0.1292)((-241.835+(0.0323)(298))+(0.756)(0+(0.0308)(298))] –F5 – F6 = 0
2[(0.0291)(298)] +137.34[(0.233)(0.0281)(298)] +(0.767)(0.0308)(298)] - 139.34[(0.1148)(0.0281)(298)] +(0.1292)[(-241.835+(0.0323)(298)] +(0.756)(0.0308)(298)] –F5 – F6 = 0
17.3436 +1234.81 – 3921.54 –F5 – F6 = 0= -2669.38
Component | DHf, 298 (kJ/mol) | DGf, 298 (kJ/mol) | Cp (kJ/mol-K) | Tc (K) | Pc (MPa) | w | Molecular weight
Oxygen | 0 | 0 | 0.0281 | 154.6 | 5.043 | 0.022 | 32
Hydrogen | 0 | 0 | 0.0291 | 33.3 | 1.297 | -0.215 | 2
Nitrogen | 0 | 0 | 0.0308 | 126.1 | 3.394 | 0.040 | 28
Water | -241.835 | -228.614 | 0.0323 | 647.3 | 22.120 | 0.344 | 18